## Slide 1: BIEN 401 Biomedical Mass Transport Class 12 Diffusion in Tissue Krogh’s Cylinder Model
notes prepared by
Dr. Louis Reis
Created on 4/2/2022

## Slide 2: Effective Diffusivities
Last class we looked at how to modify the diffusion coefficient in systems composed of heterogenous mediums so that we can use a single mass transfer expression to model the system.
We have looked at the effects of steric exclusion (), hindered diffusion (), membrane permeability (), reflection coefficients (), and sieving coefficients ().
In many of these cases, we were looking at a porous membrane (or the capillary wall).
Now we want to look at diffusion through mediums like interstitial fluid and organized tissue and see how we can develop effective diffusion coefficients for these types of environments.

## Slide 3: Effect of Cells on Diffusion
Effective diffusivity of a solute diffusing through a heterogeneous region, like blood or tissue space, that includes cells, can be modelled with Maxwell’s equation
where
is effective diffusivity in the _________
is diffusivity of the solute through the interstitial fluid space, or (for blood) plasma
is effective diffusivity in the cells
is the _________________ of cells

## Slide 4: Effect of Cells on Diffusion
If the solute is lipid-insoluble, then . The equation above simplifies into:
Where , is the void fraction.

## Slide 5: Effect of Cells on Diffusion
Alternatively, Riley et al. have developed a relationship based on Monte Carlo simulations.
Valid for

## Slide 6: Diffusion in a Random Matrix
Brinkman obtained an equation for diffusion of a solute in a random network.
where is molecular radius of the solute, is the solute’s diffusivity in the solution (without the network mesh), and is a function of the gel’s microstructure. The fraction above represents the hindered diffusion
This coefficient may need to be further modified for steric exclusion by the gel or matrix.
where is the radius of the macromolecules’ microstructure, and is the volume fraction of the macromolecular fibers. The numerator is steric exclusion, per Ogston.

## Slide 7: Diffusion in a Random Matrix
One can also use the data from Nugent and Jain. is the aqueous diffusivity of the solute. Black symbols are for normal tissue, open symbols are for tumor. is the fiber concentration in the tissue. The solid lines are a fit to a fiber matrix model of Curry and Michael
with and the solute and fiber radii, and the fiber specific volume.
The dashed lines are the Renkin model we saw last class.

## Slide 8: Krogh Tissue Cylinder
We can assume the capillaries to be arranged in parallel, and separated by an equal lateral distance. Each capillary is surrounded by a cylinder of tissue that oxygen and other solutes diffuse through. Krogh (1919) developed the cylinders to model the supply of oxygen to muscles.

## Slide 9: Krogh Tissue Cylinder
We assume that any solutes leaving the capillary and entering the tissue (e.g., oxygen) will be consumed from metabolic processes within the surrounding tissue. At some distance away from the capillary enough solute has been consumed or another capillary is closer, such that either the solute flux or solute concentration drops to zero.
In addition as solute leaves the capillary, the solute concentration in the blood and surrounding tissue will decrease. The lowest concentration of oxygen in the tissue will occur outside the venule side at the furthest edge of the cylinder (sometimes known as the lethal corner).

## Slide 10: Mass Balance insider Capillary
We will consider transport inside the capillary and in the tissue. Inside the capillary, we will ignore changes in the direction, assuming that the solute in the blood is well-stirred. The cross-sectional averaged flow velocity is . We will also treat blood as homogeneous. The flux upstream into a differential region of width is equal to the flux out downstream plus the flux out along the walls.
where the expression in square brackets on the right is the concentration difference across the capillary membrane ( is the inner capillary radius and is the capillary wall thickness), and is the overall mass transfer coefficient (refer to previous class notes). Divide by and take the limit as to get
We can use the total derivative instead of the partial derivative because inside the capillary is a function of only. is the concentration in the surrounding tissue

## Slide 11: Mass Balance inside Tissue
In the tissue, ignore diffusion in the direction as being much smaller than diffusion in the direction. (The tissue is fundamentally different from the capillary because it lacks convection that distributes the solute in the direction and moves it rapidly in the direction.) The shell balance is
where is the rate of reaction within the tissue. Divide by the volume to get
Note: this is a simplified form of the mass balance in cylindrical coordinates.)
The boundary conditions on and are

## Slide 12: Mass Balance inside Tissue
Integrate the differential equation for the tissue region once
Apply the no flux boundary condition at
Integrate again
Apply the boundary condition at

## Slide 13: Overall Mass Balance
In the last equation, we do not know the value of . We will find it from the equation for mass transport from the capillary and the knowledge that all of the the mass flux out of the capillary is consumed by the tissue.
Divide by U.
Use this in the equation to replace the left hand side of the mass transport from the capillary (slide 10)

## Slide 14: Concentration Profile in the Cylinder
Rearrange
and use this to substitute for in the tissue mass balance (slide 12) to obtain
which, substituting the expression for becomes
The equation is valid if does not go to zero anywhere in the domain. Because concentration decreases with and , the expression will first go to zero at the distal end of the capillary and .

## Slide 15: Krogh Cylinder Summary
The equation above accounts for variations in concentrations due to loss of solute down the length of the capillary (in the z-direction). It also accounts for the transport of the solute through the capillary wall.
If we assume that there is no variation in concentration in the z-direction (constant concentration in the blood), and if we are just looking at the transport of solute from the capillary surface.

## Slide 16: Critical Radius
One dimension of interest that we can pull from the Krogh cylinder model is the thickness of the tissue layer that can be supported by a capillary. The edge of the tissue represents the boundary where any tissue outside is anoxic and lacks oxygen to fulfil normal metabolic operations.
At this boundary: . If we also make the thin-wall assumption (i.e., ), then the equation becomes:
Which we can express in dimensionless form:
Note the units of:

## Slide 17: Reaction Rate of Oxygen
The Krogh cylinder model can be used for other systems and not just capillaries. It can also be used for many different solutes. But the most common solute is oxygen.
For oxygen, the Michaelis-Menten equation can be used to describe the metabolic consumption (or generation (e.g., CO2)) of solutes in the tissue space.
Where is the maximum reaction rate, and is the Michaelis constant. For many biological reactions, , so we can simplify the expression above to:

## Slide 18: Renkin-Crone Equation
Assume that solute concentration is much smaller in the tissue than in the capillary, and assume that resistance to transport by blood is much less than transport across the capillary wall, so .
then reduces to
where we have used to replace capillary velocity with capillary flow rate. Integrate with respect to and use the boundary condition that .
This is the Renkin-Crone equation. , the extraction, is the fraction of flow entering the capillary that is extracted into the tissue.

## Slide 19: Flow-limited vs. Diffusion-limited
If transport is _____ limited, it means that a large change in the diffusive flux has only a small effect on the total flux. I.e., it does not matter much how fast the diffusion is if the flow cannot carry away (or bring in) mass fast enough. This situation occurs when flow rate is small.
If the transport is _______ limited, it means that a large change in flow rate has only a small effect on the total flux. I.e., it does not matter how large the flow is if the mass cannot diffuse through the capillary wall fast enough. This situation occurs when permeability is small.

## Slide 20: Filtration from a Hollow Fiber
Consider a hollow fiber used to filter a solvent. As a result of filtration, the concentration of the solute in the bulk flow will change as solute traverses a hollow fiber filtration system. We first consider the flux of solvent, and then consider the flux of the solute. The flux of solvent from the fiber is given by
where is the reflection coefficient. The flow within the fiber into a differential volume at must be equal to plus the flow out at .
which leads to the first order differential equation
In the general case, can vary with because both the pressure gradient and the concentration difference can change with .

## Slide 21: Filtration from a Hollow Fiber
For the solute, if is the observed sieving coefficient
Divide by and take the limit as .
which can also be written, with the aid of the product rule for differentiation, as
But from the previous slide, , so
In general, we need to solve this equation and simultaneously to obtain bulk concentration and flow.
Recall:

## Slide 22: Filtration from a Hollow Fiber
If is constant, then we can integrate the equation for directly.
But from ,
Recall: